## Slide 1
01 / FIRMWARE ACCEPTANCE AND REGRESSION
SENTRY SWM-2
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
1
Stable 2.1.0 versus beta 2.3.0
Is the beta ready to become the stable release?
RELEASE RECOMMENDATION: NO-GO
Real ESP32-S3 bench + PRD traceability + reproducible evidence
Notes: Good day. My project is acceptance and regression testing of the SENTRY SWM-2 firmware, a sonar watch module running on an ESP32-S3, connected over UART on COM6.
The question I had to answer is simple: **is firmware 2.3.0 beta ready to replace 2.1.0 stable?** To answer it I tested both versions on the same real board, against the same requirements document, and compared the results.

## Slide 2
02 / METHOD
Requirements, strategy and evidence
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
2
-
PRD -> traceability matrix -> 67 defined test cases.
-
Both versions: normal, boundary, invalid-input, persistence and OTA checks.
-
101 recorded rows across 64 case IDs; not a coverage percentage.
-
40 Pass | 47 Partial | 11 Fail | 2 Investigate | 1 Not run.
-
Separate Oct 23 supplement: 4 automated tests on real firmware 2.3.0.
Notes: Everything starts from the PRD. I built a traceability matrix from the requirements to 67 defined test cases, so every test can be traced back to a requirement.
I ran acceptance and regression tests on both versions: normal behaviour, boundary values, invalid input, persistence after reboot, and OTA failures.
By the end I had **101 recorded result rows across 64 distinct case IDs**: 40 Pass, 47 Partial, 11 Fail, 2 Investigate and 1 Not run. I want to be honest about what this means: these are execution records, **not** a percentage of total planned coverage. Partial means it passed within a limited scope, not a full pass.
The testing found seven bugs, and I will show the most important ones.

## Slide 3
03 / BENCH AND SAFETY
Real hardware, manual observations
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
3
-
PC -> USB/UART COM6, 115200 8N1 -> ESP32-S3.
-
Sonar GPIO5/18 | relay GPIO8 | RGB GPIO48 | proximity LED GPIO4.
-
Buttons GPIO41/40/39/38; Wi-Fi and a local OTA fault server.
-
Observed: RGB colours, relay clicks, all state chords and Guard alarms.
-
Ruler targets at 10/20/30/50 cm; 20 cm calibration checked on both builds.
-
Low voltage, relay unloaded: no mains, no contact/load verification.
Notes: [Show the bench photo or diagram; if you want, play 15–20 s of the LED video here.]
This is the bench. An ESP32-S3 board connected over UART at 115200 baud, a Wi-Fi network with a local OTA server, an ultrasonic sonar, a relay module on GPIO8, an RGB lamp on GPIO48, four buttons on GPIO41, 40, 39 and 38, and a proximity LED on GPIO4.
Safety came first. The relay was only used at low voltage with no load, and I did not use mains or hazardous loads. I also automated the command side with a small Python helper that logs in, sends commands and captures the output, while a human was needed for physical observation: LED colours, the relay click, button presses and placing the sonar target with a ruler.
Physical observations remain manual. The new assertion-based tests are shown on slide 7. All logs were sanitised.

## Slide 4
04 / FIRMWARE UPDATE SAFETY
OTA recovery and version coverage
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
4
-
Upgrade 2.1.0 -> 2.3.0: boot and self-check passed.
-
Broken image: self-check failed; automatic rollback observed.
-
Manual rollback tested both ways; stable fallback restored and verified.
-
Both builds: garbage, truncated, corrupted and interrupted-image tests.
-
Downgrade guard and server/channel/input-error checks captured in logs.
-
Limitation: Wi-Fi loss during transfer remains inconclusive.
Notes: OTA is the riskiest part of a firmware release, so I tested it deeply.
Upgrade from 2.1.0 to 2.3.0 worked and passed the self-check. A deliberately broken image failed the self-check and the device rolled back automatically. Manual rollback worked in both directions, and I used it again to switch versions safely for the final repeat tests.
I also ran a local-server fault matrix on **both** versions: garbage, truncated, corrupted and interrupted images. They were all rejected cleanly, with no corruption, and the device recovered each time. Downgrade protection (E408) and error codes for a bad URL or version also worked.
One thing I could not prove: Wi-Fi loss in the middle of a transfer. UART is blocked during OTA, so that case stays inconclusive, and I list it as a limitation.

## Slide 5
05 / FUNCTIONAL COVERAGE
Product features verified on the bench
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
5
-
Account/password boundaries; states, lamp, relay, sonar and telemetry.
-
K1-K4 and all four state chords; EMERGENCY blocks buttons, reboot-only exit.
-
2.3.0 Guard: arm, intrusion delay, ALARM, K4 PANIC and sensor tamper.
-
CRITICAL alerts and relay response; acknowledgements and 20-alert retention.
-
2.1.0 Guard/Alert commands report E099: feature planned for 2.3.0.
-
LED/relay video and sanitized UART logs included in the complete ZIP.
Notes: Next, the features: login and states, sonar, relay, lamp, health reports, and in 2.3.0 the new Guard and Alert Center.
I ran a full account and password boundary matrix and a 136-expectation functional regression suite on both versions.
On the hardware, I physically confirmed the RGB colours, the relay click, all four buttons and every state chord, including EMERGENCY, where buttons are blocked and the only exit is a reboot.
Guard worked end to end: arming with a countdown, intrusion, a 15-second disarm window and then ALARM. ALARM opens the relay and raises a CRITICAL alert. I also tested the K4-hold PANIC, sensor tamper, and alert retention capped at 20.
On 2.1.0 these Guard and Alert commands correctly report that they are planned for 2.3.0.

## Slide 6
06 / DEFECTS, NOT ASSUMPTIONS
Seven confirmed findings
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
6
BUG-01
Both
distance 20 rejected; PRD allows 1-20.
BUG-02
Both
Relay pulse below 100 ms accepted.
BUG-03
2.1.0
Health interval 300 s rejected; beta accepts it.
BUG-04
Both
Relay cycles: double-count / reboot loses increment.
BUG-05
2.1.0
Lamp timer message says ms instead of s (cosmetic).
BUG-06
2.3.0
Wrong-PIN count accumulates until reboot: false-alarm risk.
BUG-07
Both
Documented calibration-reset syntax rejected.
Most are existing defects, not beta regressions. Debug-secret finding disclosed and redacted.
Notes: [This is the most important slide; slow down.]
Seven bugs. The key point is that most are **not** beta regressions.
- **BUG-01:** `distance 20` is rejected, although the PRD range is 1 to 20. Both versions.
- **BUG-02:** `relay pulse` accepts values below the PRD minimum of 100 ms. Both versions.
- **BUG-04:** the relay cycle counter miscounts. On 2.1.0 every switch adds two; on 2.3.0 the last increment is lost across a reboot.
- **BUG-03:** a health interval of 300 seconds is rejected on 2.1.0 but accepted on 2.3.0. This is stable-only, so 2.3.0 actually fixes it.
- **BUG-05:** a cosmetic one on 2.1.0: the lamp timer message says "ms" but the timing is in seconds.
- **BUG-06:** new in 2.3.0 Guard. The wrong-PIN counter never resets. After three wrong PINs over the device's lifetime since boot, a single typo raises ALARM. A reboot clears it.
- **BUG-07:** the documented command `distance calibrate reset` returns an error on both versions. The undocumented `distance reset` works.
As a bonus, during authorised security exploration I found a leaked debug sudo password and a hidden selftest command. I reported them responsibly and redacted them everywhere in my evidence.

## Slide 7
07 / OCTOBER 23 LIVE RUN
Automated regression: real board, real assertions
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
7
Firmware 2.3.0: 4 tests | 1 PASS | 3 FAIL | 0 errors
FAIL
BUG-01: distance 20 must be accepted.
FAIL
BUG-02: relay pulse 99 ms must be rejected.
PASS
BUG-03: health 300 s accepted; 301 s rejected.
FAIL
BUG-07: distance calibrate reset must work.
Python unittest + pyserial | sanitized transcript + assertions + JSON
Cleanup verified: relay closed; starting health interval restored.
7 offline harness checks passed. Live suite validated on 2.3.0 only; physical outputs remain manual.
Notes: To make recurring failures easy to retest, I delivered a small Python unittest
suite that communicates with the actual board over UART. It contains four
tests with automatic assertions against the PRD, including valid boundaries
and neighbouring invalid inputs.
On firmware 2.3.0, the live run produced one passing test and three failing
tests, with no setup or cleanup errors. Distance count 20, the 99-millisecond
relay pulse and the documented calibration-reset command reproduced BUG-01,
BUG-02 and BUG-07. The health interval test passed: 300 seconds was accepted
and 301 rejected.
These red results are evidence of firmware defects, not a broken runner.
The runner records sanitised UART transcripts, assertion results and a JSON
summary. It closes the relay and restores the original health interval.
Seven offline tests also passed to validate the runner itself.
The new suite was hardware-validated on 2.3.0 only. It does not claim physical
relay-contact verification or sonar accuracy, and the reset test checks syntax
from an initially zero offset. These four tests supplement, rather than replace,
the earlier 101 execution rows.

## Slide 8
08 / RECOMMENDATION AND LIMITS
Decision: do not promote 2.3.0 yet
SENTRY SWM-2 | Zolotykh | Defense: 23 Oct 2026 | Evidence: 19-23 Oct
8
-
NO-GO: confirmed PRD violations plus Guard false-alarm risk.
-
Fix BUG-01/02/04/06; assess remaining defects and rerun regression tests.
-
Known failures stay red: the suite must not accept incorrect firmware.
-
Not run: 5/300 cm calibration targets; relay contacts under real load.
-
Inconclusive: Wi-Fi loss during OTA. New automated suite: beta-only live run.
-
Delivered: report, traceability, bugs, logs, video, test code and rerun guide.
Notes: My recommendation is **NO-GO for promoting 2.3.0 to stable at this time.**
BUG-01, BUG-02 and BUG-04 violate PRD limits on both versions, and BUG-06 adds a real false-alarm risk in the new Guard feature. This is a recommendation about this specific build, not a claim that 2.3.0 is generally worse than 2.1.0. Retest after fixes.
Gaps remain, and I state them openly: the calibrate boundaries of 5 and 300 cm were not run, relay contact behaviour under real load was not measured, and Wi-Fi loss during OTA is inconclusive.
Lessons: test against the requirements, not against assumptions; run the same boundaries on every version, because that is how you separate old defects from regressions; and keep evidence sanitised and reproducible. I corrected one of my own early mistakes along the way, a calibrate-reset result I had first misread, which is why re-checking matters.
Thank you. I am ready for questions.